## Slide 1: Virtual Memory: Concepts CENG331 - Computer Organization
Adapted from slides of the textbook: http://csapp.cs.cmu.edu/

## Slide 2: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 3: A System Using Physical Addressing
Used in “simple” systems like embedded microcontrollers in devices like cars, elevators, and digital picture frames
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4

## Slide 4: A System Using Virtual Addressing
Used in all modern servers, laptops, and smart phones
One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 5: Address Spaces
Linear address space: Ordered set of contiguous non-negative integer addresses: {0, 1, 2, 3 … }
Virtual address space: Set of N = 2n virtual addresses {0, 1, 2, 3, …, N-1}
Physical address space: Set of M = 2m physical addresses {0, 1, 2, 3, …, M-1}
Clean distinction between data (bytes) and their attributes (addresses)
Every byte in main memory has one physical address and zero or more virtual addresses

## Slide 6: Why Virtual Memory (VM)?
Uses main memory efficiently
  Use DRAM as a cache for parts of a virtual address space
Simplifies memory management
  Each process gets the same uniform linear address space
Isolates address spaces
  One process can’t interfere with another’s memory
  User program cannot access privileged kernel information and code

## Slide 7: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 8: VM as a Tool for Caching
Conceptually, virtual memory is an array of N contiguous bytes stored on disk.
The contents of the array on disk are cached in physical memory (DRAM cache)
  These cache blocks are called pages (size is P = 2p bytes)
PP 2m-p-1
Physical memory
Empty
Empty
Uncached
VP 0
VP 1
VP 2n-p-1
Virtual memory
Unallocated
Cached
Uncached
Unallocated
Cached
Uncached
PP 0
PP 1
Empty
Cached
0
N-1
M-1
0
Virtual pages (VPs)
stored on disk
Physical pages (PPs)
cached in DRAM

## Slide 9: DRAM Cache Organization
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 10x slower than SRAM
  Disk is about 10,000x slower than DRAM
Consequences
  Large page (block) size: typically 4-8 KB, sometimes 4 MB
  Fully associative
    Any VP can be placed in any PP
    Requires a “large” mapping function – different from CPU caches
  Highly sophisticated, expensive replacement algorithms
    Too complicated and open-ended to be implemented in hardware
  Write-back rather than write-through

## Slide 10: Enabling Data Structure: Page Table
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  Per-process kernel data structure in DRAM
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 11: Page Hit
Page hit: reference to VM word that is in physical memory (DRAM cache hit)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 12: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 13: Handling Page Fault
Page miss causes page fault (an exception)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 14: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 15: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address

## Slide 16: Handling Page Fault
Page miss causes page fault (an exception)
Page fault handler selects a victim to be evicted (here VP 4)
Offending instruction is restarted: page hit!
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Key point: Waiting until the miss to copy the page to DRAM is known as demand paging

## Slide 17: Allocating Pages
Allocating a new page (VP 5) of virtual memory.
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 3
Virtual memory
(disk)
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
VP 5

## Slide 18: Locality to the Rescue Again!
Virtual memory seems terribly inefficient, but it works because of locality.
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with better temporal locality will have smaller working sets
If (working set size < main memory size)
  Good performance for one process after compulsory misses
If ( SUM(working set sizes) > main memory size )
  Thrashing: Performance meltdown where pages are swapped (copied) in and out continuously

## Slide 19: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 20: VM as a Tool for Memory Management
Key idea: each process has its own virtual address space
  It can view memory as a simple linear array
  Mapping function scatters addresses through physical memory
    Well-chosen mappings can improve locality
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 21: VM as a Tool for Memory Management
Memory allocation
  Each virtual page can be mapped to any physical page
  A virtual page can be stored in different physical pages at different times
Sharing code and data among processes
  Map virtual pages to the same physical page (here: PP 6)
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 22: Simplifying Linking and Loading
Linking
  Each program has similar virtual address space
  Code, stack, and shared libraries always start at the same address
Loading
  execve allocates virtual pages for .text and .data sections & creates PTEs marked as invalid
  The .text and .data sections are copied, page by page, on demand by the virtual memory system
Kernel virtual memory
Memory-mapped region for
shared libraries
Run-time heap
(created by malloc)
User stack
(created at runtime)
Unused
0
%rsp
(stack
pointer)
Memory
invisible to
user code
brk
0x400000
Read/write segment
(.data, .bss)
Read-only segment
(.init, .text, .rodata)
Loaded
from
the
executable
file

## Slide 23: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 24: VM as a Tool for Memory Protection
Extend PTEs with permission bits
Page fault handler checks these before remapping
  If violated, send process SIGSEGV (segmentation fault)
Process i:
Address
READ
WRITE
PP 6
Yes
No
PP 4
Yes
Yes
PP 2
Yes
VP 0:
VP 1:
VP 2:
•
•
•
Process j:
Yes
SUP
No
No
Yes
Address
READ
WRITE
PP 9
Yes
No
PP 6
Yes
Yes
PP 11
Yes
Yes
SUP
No
Yes
No
VP 0:
VP 1:
VP 2:
Physical
Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
EXEC
Yes
EXEC
Yes
Yes
Yes
Yes
No
SUP bit set to 1 indicates that the process must be running in SUPervisor mode to access.
Processes running in user mode can only access pages with SUP set to 0.

## Slide 25: Today
Address spaces
VM as a tool for caching
VM as a tool for memory management
VM as a tool for memory protection
Address translation

## Slide 26: VM Address Translation
Virtual Address Space
  V = {0, 1, …, N–1}
Physical Address Space
  P = {0, 1, …, M–1}
Address Translation
  MAP: V  P U {}
  For virtual address a:
    MAP(a) = a’ if data at virtual address a is at physical address a’ in P
    MAP(a) =  if data at virtual address a is not in physical memory
      Either invalid or stored on disk

## Slide 27: Summary of Address Translation Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number

## Slide 28: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Physical page number (PPN)
Physical page offset (PPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register
(PTBR)
Page table
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
0
p-1
p
n-1
0
p-1
p
m-1

## Slide 29: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5

## Slide 30: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 31: Integrating VM and Cache
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 32: Speeding up Translation with a TLB
Page table entries (PTEs) are cached in L1 like any other memory word
  PTEs may be evicted by other data references
  PTE hit still requires a small L1 delay
Solution: Translation Lookaside Buffer (TLB)
  Small set-associative hardware cache in MMU
  Maps virtual page numbers to physical page numbers
  Contains complete page table entries for small number of pages

## Slide 33: Accessing the TLB
MMU uses the VPN portion of the virtual address to access the TLB:
TLB tag (TLBT)
TLB index (TLBI)
0
p-1
p
n-1
VPO
VPN
p+t-1
p+t
PTE
tag
v
…
PTE
tag
v
Set 0
PTE
tag
v
PTE
tag
v
Set 1
PTE
tag
v
PTE
tag
v
Set T-1
T = 2t sets
TLBI selects the set
TLBT matches tag of line within set

## Slide 34: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3

## Slide 35: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare. Why?

## Slide 36: Multi-Level Page Tables
Suppose:
  4KB (212) page size, 48-bit address space, 8-byte PTE
Problem:
  Would need a 512 GB page table!
    248 * 2-12 * 23 = 239 bytes
Common solution: Multi-level page table
Example: 2-level page table
  Level 1 table: each PTE points to a page table (always memory resident)
  Level 2 table: each PTE points to a page (paged in and out like any other data)
Level 1
Table
...
Level 2
Tables
...

## Slide 37: A Two-Level Page Table Hierarchy
Level 1
page table
...
Level 2
page tables
VP 0
...
VP 1023
VP 1024
...
VP 2047
Gap
0
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null
PTEs
PTE 1023
1023
unallocated
pages
VP 9215
Virtual
memory
(1K - 9)
null PTEs
PTE 0
PTE 1
PTE 2 (null)
PTE 3 (null)
PTE 4 (null)
PTE 5 (null)
PTE 6 (null)
PTE 7 (null)
PTE 8
2K allocated VM pages
for code and data
6K unallocated VM pages
1023 unallocated pages
1 allocated VM page
for the stack
32 bit addresses, 4KB pages, 4-byte PTEs

## Slide 38: Translating with a k-level Page Table
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
Level 1
page table
Level 2
page table
Level k
page table

## Slide 39: Summary
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection by providing a convenient interpositioning point to check permissions

## Slide 40: Virtual Memory: Systems CENG331 - Computer Organization
Instructors:
Murat Manguoglu (Section 1)
Erol Sahin (Section 2)
Adapted from slides of the textbook: http://csapp.cs.cmu.edu/

## Slide 41: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 42: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 43: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 44: 1. Simple Memory System TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set

## Slide 45: 2. Simple Memory System Page Table
Only show first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN

## Slide 46: 3. Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 47: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36

## Slide 48: Address Translation Example #2
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem

## Slide 49: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem

## Slide 50: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 51: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge

## Slide 52: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 53: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE

## Slide 54: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table. Significant fields:
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 1 PTEs only).
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
XD: Disable or enable instruction fetches from all pages reachable from this PTE.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63

## Slide 55: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page. Significant fields:
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
XD: Disable or enable instruction fetches from this page.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63

## Slide 56: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 57: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available next
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
40
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check

## Slide 58: Virtual Address Space of a Linux Process
Kernel code and data
Memory mapped region
for shared libraries
Runtime heap (malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
%rsp
Process
virtual
memory
brk
Physical memory
Identical for each process
Process-specific data
structs (ptables,
task and mm structs, kernel stack)
Kernel
virtual
memory
0x00400000
Different for each process

## Slide 59: Linux Organizes VM as Collection of “Areas”
vm_next
vm_next
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
Text
Data
Shared libraries
0
pgd:
  Page global directory address
  Points to L1 page table
vm_prot:
  Read/write permissions for this area
vm_flags
  Pages shared with other processes or private to this process
vm_flags
vm_flags
vm_flags

## Slide 60: Linux Page Fault Handling
read
1
write
2
read
3
vm_next
vm_next
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
text
data
shared libraries
vm_flags
vm_flags
vm_flags
Segmentation fault:
accessing a non-existing page
Normal page fault
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)

## Slide 61: Today
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 62: Memory Mapping
VM areas initialized by associating them with disk objects.
  Process is known as memory mapping.
Area can be backed by (i.e., get its initial values from) :
  Regular file on disk (e.g., an executable object file)
    Initial page bytes come from a section of a file
  Anonymous file (e.g., nothing)
    First fault will allocate a physical page full of 0's (demand-zero page)
    Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

## Slide 63: Sharing Revisited: Shared Objects
Process 1 maps the shared object.
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory

## Slide 64: Sharing Revisited: Shared Objects
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Process 2 maps the shared object.
Notice how the virtual addresses can be different.

## Slide 65: Sharing Revisited: Private Copy-on-write (COW) Objects
Two processes mapping a private copy-on-write (COW) object.
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Private
copy-on-write
area

## Slide 66: Sharing Revisited: Private Copy-on-write (COW) Objects
Instruction writing to private page triggers protection fault.
Handler creates new R/W page.
Instruction restarts upon handler return.
Copying deferred as long as possible!
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Copy-on-write
Write to private
copy-on-write
page

## Slide 67: The fork Function Revisited
VM and memory mapping explain how fork provides private address space for each process.
To create virtual address for new new process
  Create exact copies of current mm_struct, vm_area_struct, and page tables.
  Flag each page in both processes as read-only
  Flag each vm_area_struct in both processes as private COW
On return, each process has exact copy of virtual memory
Subsequent writes create new pages using COW mechanism.

## Slide 68: The execve Function Revisited
To load and run a new program a.out in the current process using execve:
Free vm_area_struct’s and page tables for old areas
Create vm_area_struct’s and page tables for new areas
  Programs and initialized data backed by object files.
  .bss and stack backed by anonymous files .
Set PC to entry point in .text
  Linux will fault in code and data pages as needed.
Memory mapped region
for shared libraries
Runtime heap (via malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
Private, demand-zero
libc.so
.data
.text
Shared, file-backed
Private, demand-zero
Private, demand-zero
Private, file-backed
a.out
.data
.text

## Slide 69: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
Map len bytes starting at offset offset of the file specified by file description fd, preferably at address start
  start: may be 0 for “pick an address”
  prot: PROT_READ, PROT_WRITE, ...
  flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Return a pointer to start of mapped area (may not be start)

## Slide 70: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
Process virtual memory
Disk file specified by
file descriptor fd
len bytes
offset
(bytes)
0
0

## Slide 71: Example: Using mmap to Copy Files
/* mmapcopy driver */
int main(int argc, char **argv)
{
struct stat stat;
int fd;
/* Check for required cmd line arg */
if (argc != 2) {
printf("usage: %s <filename>\n",
argv[0]);
exit(0);
}
/* Copy input file to stdout */
fd = Open(argv[1], O_RDONLY, 0);
Fstat(fd, &stat);
mmapcopy(fd, stat.st_size);
exit(0);
}
Copying a file to stdout without transferring data to user space .
#include "csapp.h"
void mmapcopy(int fd, int size)
{
/* Ptr to memory mapped area */
char *bufp;
bufp = Mmap(NULL, size,
PROT_READ,
MAP_PRIVATE,
fd, 0);
Write(1, bufp, size);
return;
}
mmapcopy.c
mmapcopy.c