## Slide 1: Floating Point
Carnegie Mellon

## Slide 2: Today: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 3: Fractional binary numbers
Carnegie Mellon
What is 1011.1012?

## Slide 4: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
Carnegie Mellon
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 5: Fractional Binary Numbers: Examples
Carnegie Mellon
Value Representation
5 3/4 101.112
2 7/8 010.1112
1 7/16 001.01112
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 6: Representable Numbers
Carnegie Mellon
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
    Limited range of numbers (very small values? very large?)

## Slide 7: Today: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 8: IEEE Floating Point
Carnegie Mellon
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard

## Slide 9: Floating Point Representation
Carnegie Mellon
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 10: Precision options
Carnegie Mellon
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 11: “Normalized” Values
Carnegie Mellon
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
v = (–1)s M 2E

## Slide 12: “Normalized” Values
Carnegie Mellon
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (Exp: 1…254, E: -126…127)
    Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E

## Slide 13: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac
v = (–1)s M 2E
E = Exp – Bias

## Slide 14: Denormalized Values
Carnegie Mellon
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of E = 0 – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
v = (–1)s M 2E
E = 1 – Bias

## Slide 15: Denormalized Values
Carnegie Mellon
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of E = 0 – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced
v = (–1)s M 2E
E = 1 – Bias

## Slide 16: Special Values
Carnegie Mellon
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = + , 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1), − , 0

## Slide 17: Visualization: Floating Point Encodings
Carnegie Mellon
+
−
-0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 18: Today: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 19: Tiny Floating Point Example
Carnegie Mellon
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 20: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 21: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 22: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 23: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 24: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 25: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 26: Distribution of Values
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
8 values
s | exp | frac
1 | 3-bits | 2-bits

## Slide 27: Distribution of Values (close-up view)
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 28: Special Properties of the IEEE Encoding
Carnegie Mellon
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 29: Today: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 30: Floating Point Operations: Basic Idea
Carnegie Mellon
x +f y = Round(x + y)
X f y = Round(x y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac

## Slide 31: FP Multiplication
Carnegie Mellon
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 32: Floating Point Addition
Carnegie Mellon
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 33: Today: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 34: Floating Point in C
Carnegie Mellon
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 35: Interesting Numbers
Carnegie Mellon
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} x 2– {126,1022}
  Single ≈ 1.4 x 10–45
  Double ≈ 4.9 x 10–324
Largest Denormalized 00…00 11…11 (1.0 – ε) x 2– {126,1022}
  Single ≈ 1.18 x 10–38
  Double ≈ 2.2 x 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 x 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ε) x 2{127,1023}
  Single ≈ 3.4 x 1038
  Double ≈ 1.8 x 10308
{single,double}

## Slide 36: Mathematical Properties of FP Add
Carnegie Mellon
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
Yes
No
Almost
Almost

## Slide 37: Mathematical Properties of FP Mult
Carnegie Mellon
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 38: Ariane 5
  Exploded 37 seconds after liftoff
  Cargo worth $500 million
Why
  Computed horizontal velocity as floating point number
  Converted to 16-bit integer
  Worked OK for Ariane 4
  Overflowed for Ariane 5
    Used same software

## Slide 39: Floating Point Puzzles
Carnegie Mellon
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN

## Slide 40: Summary
Carnegie Mellon
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers

## Slide 41: Additional Slides
Carnegie Mellon

## Slide 42: Rounding
Carnegie Mellon
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $2 $1 $2 –$1
  Round down (−) $1 $2 $1 $2 –$2
  Round up (+) $1 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2
Rounding mode changes only the rounding of midway values such as 1.5, 0.5, or -2.5.
Rounding of other values such as 1.4, 2.51, or -3.49 is not affected!

## Slide 43: Rounding: Towards Zero
Carnegie Mellon
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Each value is rounded to the closest number
Midway values are rounded to the closest number towards the ZERO direction
This mode reduces the variance of the data and changes mean of the numbers

## Slide 44: Rounding: Round down (−)
Carnegie Mellon
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Each value is rounded to the closest number
Midway values are rounded to the closest number towards −INFINITY direction
This mode does not affect the variance of the data and but decreases the mean of the numbers

## Slide 45: Rounding: Round up (+)
Carnegie Mellon
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Each value is rounded to the closest number
Midway values are rounded to the closest number towards +INFINITY direction
This mode does not affect the variance of the data and but increases the mean of the numbers

## Slide 46: Rounding: Nearest Even
Carnegie Mellon
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Each value is rounded to the closest number
Midway values are rounded to the closest EVEN number
This mode does not change the statistical properties (such as mean and variance) of the numbers,
Default rounding mode

## Slide 47: 4 modes of rounding – for midway values
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Towards zero
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Round down (−)
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Round up (+)
0
1
2
-1
-2
-3
3
-2.5
-1.5
-0.5
0.5
1.5
2.5
Nearest even (default)

## Slide 48: Closer Look at Round-To-Even
Carnegie Mellon
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    7.8949999 7.89 (Less than half way)
    7.8950001 7.90 (Greater than half way)
    7.8950000 7.90 (Half way—round up)
    7.8850000 7.88 (Half way—round down)

## Slide 49: Rounding Binary Numbers
Carnegie Mellon
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 50: Creating Floating Point Number
Carnegie Mellon
Steps
  Normalize to have leading 1
  Round to fit within fraction
  Postnormalize to deal with effects of rounding
Case Study
  Convert 8-bit unsigned numbers to tiny floating point format
  Example Numbers
  128 10000000
  15 00001101
  33 00010001
  35 00010011
  138 10001010
  63 00111111
s | exp | frac
1 | 4-bits | 3-bits

## Slide 51: Normalize
Carnegie Mellon
Requirement
  Set binary point so that numbers of form 1.xxxxx
  Adjust all to have leading one
    Decrement exponent as shift left
  Value Binary Fraction Exponent
  128 10000000 1.0000000 7
  15 00001101 1.1010000 3
  17 00010001 1.0001000 4
  19 00010011 1.0011000 4
  138 10001010 1.0001010 7
  63 00111111 1.1111100 5
s | exp | frac
1 | 4-bits | 3-bits

## Slide 52: Rounding
Carnegie Mellon
Round up conditions
  Round = 1, Sticky = 1 ➙ > 0.5
  Guard = 1, Round = 1, Sticky = 0 ➙ Round to even
  Value Fraction GRS Incr? Rounded
  128 1.0000000 000 N 1.000
  15 1.1010000 100 N 1.101
  17 1.0001000 010 N 1.000
  19 1.0011000 110 Y 1.010
  138 1.0001010 011 Y 1.001
  63 1.1111100 111 Y 10.000
1.BBGRXXX
Guard bit: LSB of result
Round bit: 1st bit removed
Sticky bit: OR of remaining bits

## Slide 53: Postnormalize
Carnegie Mellon
Issue
  Rounding may have caused overflow
  Handle by shifting right once & incrementing exponent
  Value Rounded Exp Adjusted Result
  128 1.000 7 128
  15 1.101 3 15
  17 1.000 4 16
  19 1.010 4 20
  138 1.001 7 134
  63 10.000 5 1.000/6 64

## Slide 54: Rounding in C
http://www.gnu.org/s/libc/manual/html_node/Rounding-Functions.html
  double rint (double x), float rintf (float x), long double rintl (long double x) These functions round x to an integer value according to the current rounding mode. See Floating Point Parameters, for information about the various rounding modes. The default rounding mode is to round to the nearest integer; some machines support other modes, but round-to-nearest is always used unless you explicitly select another.
  If x was not initially an integer, these functions raise the inexact exception.
http://www.gnu.org/s/libc/manual/html_node/Floating-Point-Parameters.html#Floating-Point-Parameters
  FLT_ROUNDS characterizes the rounding mode for floating point addition. Standard rounding modes:
    -1: The mode is indeterminable.
    0: Rounding is towards zero.
    1: Rounding is to the nearest number.
    2: Rounding is towards positive infinity.
    3:Rounding is towards negative infinity.

## Slide 55: Using f instead of i?
What would happen?
What would happen if we had a “short float” representation?
float f=0;
for (f=0;f<10000000000.0;f+=1)
printf(“%f\n”);
s | exp | frac
1 | 7-bits | 8-bits

## Slide 56: Quiz 1
Write a C expression that will yield a word consisting of the least significant byte of x and the remaining bytes of y. For instance, for operands x = 0x89ABCDEF and y = 0x76543210, the Result = 0x765432EF. Your code should work for all word sizes (short/int/long). Write the C expression that would be inserted into the blank shown below:
Result = (x&0xFF)|(y&~0xFF);

## Slide 57: Quiz 2
Smallest Positive Nonzero number as double
  0 00000000000 0000000000000000000000000000000000000000000000000001
  Value = (-1)^0 * 2^(-52) *2^(1-1023) = 2^(-1074)
Largest positive Non-infinity number as double
  0 11111111110 11111111111111111111111111111111111111111111111111111
  Value = (-1)^0 * (2-2^(-52)) *2^((2^11-2)-(2^10-1))
  = (2-2^(-52)) *2^((2^11-2)-(2^10-1))
  =(2-2^(-52)) *2^(2^10-1)
  = 2^(2^10) - 2^(-52)+2^10-1)
  = 2^1024 – 2^(-52+1023) = 2^1024 – 2^971
s | exp | frac
1 | 11-bits | 52-bits
  e= 11 bits => Bias=2^(e-1)-1 = 2^10-1= 1023

## Slide 58: Quiz 2
Float representation of 1024.75 in Hex
Binary representation
  1024.75 = 10000000000.11
  = 1.000000000011 * 2^10
  M=1.000000000011
    frac = 00000000001100000000000
  E=10
    exp= Bias + E = 137 = 10001001
0 10001001 00000000001100000000000
0100 0100 1000 0000 0001 1000 0000 0000
0x44801800
s | exp | frac
1 | 8-bits | 23-bits
  e= 8 bits => Bias=2^(e-1)-1 = 2^7-1= 127

## Slide 59: Using Union to Access Bit Patterns
typedef union {
float f;
unsigned u;
} bit_float_t;
float bit2float(unsigned u) {
bit_float_t arg;
arg.u = u;
return arg.f;
}
unsigned float2bit(float f) {
bit_float_t arg;
arg.f = f;
return arg.u;
}
Same as (float) u ?
Same as (unsigned) f ?
 | u |  |  |  | 
 | f |  |  |  | 
0 |  |  |  | 4 | 

## Slide 60: Quiz 2
#include <stdio.h>
union {
float f;
unsigned u;
} x;
int main(){
x.f=1024.75;
printf(”Hex representation: %x\n”,x.u);
}
s | exp | frac
1 | 8-bits | 23-bits
Float representation of 1024.75 in Hex

## Slide 61: Quiz 2
#include <stdio.h>
union {
double d;
long unsigned u;
} x;
int main(){
x.u=0x1;
printf("Double representation: %.1000g\n",x.d);
}
Smallest Positive Nonzero number as double
  0 00000000000 0000000000000000000000000000000000000000000000000001
  = 0x1 in hex
s | exp | frac
1 | 11-bits | 52-bits